## Slide 1
Aguila Global

## Slide 2
Content
Background
Theoretical Foundation
Oil & Gas production effects
Tubing energy management
Reservoir energy management
MPFV® applications in oil & gas wells
Technical proposal

## Slide 3
The Flow Pattern Enhancer MPFV® is a mechanical system, created for downhole applications, it is made with corrosion-resistant materials and its main components are erosion-resistant.
The MPFV® have 3 main components engineered to specific conditions of each well
Primary Expander is designed to controlling the pressure and flow of hydrocarbons coming from reservoir,
Venturi Neck generates a homogeneous flow and prevents slippage of gas and liquid in well tubing, both parts, Venturi Neck and Primary Expander, are coupled to retrievable packer,
Retrievable Packer fixes hermetically entire system against production tubing.
Background

## Slide 4
Theoretical Foundation
The Venturi-type flow pattern enhancer system MPFV®
  The MPFV®’s operation is like the jet effect in a hydraulic pump, velocity of flow increases inversely proportional to pressure in the Venturi’s neck troth. The reservoir´s fluid is the only source of energy and flows through the MPFV® like power fluid in a Jet pump, that is why MPFV® is not consider a production artificial system.
  The Venturi effect can be calculated by combining the Bernoulli’s principle and the continuity equation.

## Slide 5
Liquid Loading
  In mature gas fields Intermittent flow patterns are presented by a periodic flow of gas and liquid with a large variation of flow rate and pressure into the well tubing, this instability generates unexpected interruptions in well production.
Homogeneous Flow
Annular Flow
Mist
Flow
Liquid film
Gas flow
The appropriate selection of Venturi system would help to hydrocarbon flow, decreasing the energy losses by the intermittent flow pattern, accelerating and mixing the gas and liquid phases, with a lower energy requirement.
Liquid loading

## Slide 6
Tubing Energy Management
MPFV® is used in wells to:
Increase flow velocity avoiding slippage of gas and liquid phases.
Mixes two or more phases in homogeneous flow.
Reduces pressure drops in the production tubing.
Avoids liquids accumulation in the bottomhole.
No more freezing piping's and Methane Hydrates formation in the surface.

## Slide 7
Tubing Energy Management
SMOOTH FLOW
WITH MPFV®
MPFV®
HOMOGENEOUS FLOW WITHOUT LIQUID LOADING
MIST
HIGH VELOCITY ZONE
TURBULENT FLOW
NO MPFV®
UNSTABLE FLOW WITH LIQUID LOADING
WELL
SLUG

## Slide 8
Reservoir Energy Management
Reduces the effects of turbulent flow in porous media such as:
High pressure drops in the porous media.
Separation and segregation of the gas and liquid phases.
Conification of water.
Gas condensation in a porous media, blocking the flow to well.
Solids Production

## Slide 9
Reservoir Energy Management
WITHOUT MPFV®
WITH MPFV®
TURBULENT OR CHAOTIC FLOW AFFECTS
DROP OF PRESSURE AND INCREASES THE RESERVOIR DECLINATION.
RESERVOIR

## Slide 10
Uses
  MPFV® has been installed on 700 wells of several fields of PEMEX.
IMP has given this service to Pemex since 2009 in the Northern and Southern regions.
The tool is manufactured for standard tubing sizes as 2 7/8”, 3 ½” and 4 ½” nominal diameter.
The MPFV® Service includes wells simulation, design, manufacturing, installation and maintenance.
MPFV® is installed and retrieved of production tubing just with help of a slickline unit with standard accessories.

## Slide 11
Oil and Gas Wells
WELL “A”
The pressure gradient produced after installation of the MPFV® was more stable than before, this indicates that flow pattern was improved, reducing pressure losses in well.
GOALS:
Homogeneous flow with reduction of pressure drop in the production tubing.
PRESSURE GRADIENT (Kg/cm2 m)
MESUERE DEPTH (METERS)
NO MPFV®
WITH MPFV®

## Slide 12
Unconventional Oil reservoirs
WELL “B”
The MPFV® applied in unconventional reservoirs for production maintenance.
The MPFV® changed the decline trend of production.
The MPFV® increased recovered production by 4,653 barrels in 154 days.
Increases the productive life of the well
GOALS:
Increase Oil Net Production (Np).
Oil flowrate (BPD)
Time (Days)
Marginal Flowrate
WITHOUT MPFV®
WITH MPFV®
WITHOUT MPFV®
WITH MPFV®

## Slide 13
Water Control
WITHOUT MPFV®
WITH MPFV®
WITHOUT MPFV®
WITH MPFV®
With MPFV® since
Depth of installation
Well head pressure Charts
Water
%
Water
%
Water
%
Water
%
The MPFV® applied in oil reservoirs for control of water production and stabilization of well head pressure.
A wide variation in well head pressure is identified, from 23 to 37 kg / cm2, with a water cut of 60%.
The MPFV system stabilized pressure from 14 to 15 kg/cm2 and increased net oil production from 145 to 230 bpd.

## Slide 14
Gas Wells - Analysis
Well | Set-up date | Ø Venturi y Exp. (in) | Depth (m)
1A | 06/11/2009 | 18x20 | 1911
1B | 29/11/2009 | 16x18 | 2006
1C | 24/12/2009 | 12x14 | 2208
1D | 27/01/2010 | 14x16 | 1946
1E | 18/02/2010 | 20x22 | 2317
1F | 21/02/2010 | 18x20 | 1800
1G | 29/03/2010 | 10x12 | 3178
1H | 22/04/2010 | 10x12 | 2762
1I | 23/07/2010 | 12x14 | 1680
1J | 09/09/2010 | 14x16 | 2383
Gas wells (10) from the Northern Region in the Burgos Basin have been selected for an economic analysis with the MPFV®.

## Slide 15
Gas Wells – Economic Analysis
An average of 24 months of production was considered for the analysis with the MPFV®.
Well | Gp Increase (mmcf) | IPV (MUSD) | NPV (MUSD) | NPV/IPV (MUSD)
1A | 597 | 295 | 1,207 | 4.09
1B | 867 | 414 | 1,761 | 4.25
1C | 97 | 74 | 175 | 2.37
1D | 560 | 721 | 3,189 | 4.42
1E | 923 | 440 | 1,880 | 4.27
1F | 299 | 164 | 594 | 3.62
1G | 318 | 174 | 639 | 3.68
1H | 182 | 111 | 346 | 3.13
1I | 171 | 106 | 324 | 3.06
1J | 437 | 225 | 877 | 3.90
Mean | 445 | 272 | 1,099 | 3.68

## Slide 16
Performance production Well 1G
Chart: Well 1G Production
| 40238.000000 | 40269.000000 | 40299.000000 | 40330.000000 | 40360.000000 | 40391.000000 | 40422.000000 | 40452.000000 | 40483.000000 | 40513.000000 | 40544.000000 | 40575.000000 | 40603.000000 | 40634.000000 | 40664.000000 | 40695.000000 | 40725.000000 | 40756.000000 | 40787.000000 | 40817.000000 | 40848.000000 | 40878.000000 | 40909.000000 | 40940.000000 | 40969.000000
Production with Venturi | 0.449 | 1.1449 | 0.8028 | 0.6735 | 0.7956 | 0.3122 | 0.4967 | 0.3588 | 0.3465 | 0.6877 | 0.7997 | 0.3897 | 0.4747 | 0.4938 | 0.4503 | 0.4514 | 0.4762 | 0.538 | 0.4818 | 0.3191 | 0.316 | 0.3116 | 0.2842 | 0.2825 | 0.2301
Well 1G without Venturi | 1.3335 | 1.1249 | 0.7496 | 0.449 | 0.33098 | 0.22898 | 0.15844 | 0.10965 | 0.075891 | 0.052534 | 0.03637 | 0.025183 | 0.017439 | 0.012078 | 0.008367 | 0.005796 | 0.004016 | 0.002783 | 0.001929 | 0.001337 | 0.000927 | 0.000643 | 0.000446 | 0.000309 | 0.000214 | 0.000149 | 0.000103 | 7.2e-05
Well 1G before set up Venturi | 1.3335 | 1.1249 | 0.7496 | 0.449 | 0.33098
Well 1G adjusted production | 0.9863 | 0.88063 | 0.7954 | 0.72522 | 0.66642 | 0.61644 | 0.57343 | 0.53603 | 0.50321 | 0.47418 | 0.44832 | 0.42513 | 0.40422 | 0.38527 | 0.36802 | 0.35225 | 0.33777 | 0.32444 | 0.31212 | 0.3007 | 0.29009 | 0.2802 | 0.27096 | 0.26231
Chart: Well 1G Production
| Dec-13 | Jan-14 | Feb-14 | Mar-14 | Apr-14 | May-14 | Jun-14 | Jul-14 | Aug-14 | Sept-14 | Oct-14 | Nov-14 | Dec-14 | Jan-15 | Feb-15 | Mar-15 | Apr-15 | May-15 | Jun-15 | Jul-15 | Aug-15 | Sept-15 | Oct-15 | Nov-15 | Dec-15 | Jan-16 | Feb-16 | Mar-16
Cuitlahuac 869 CV | 0.449 | 1.1449 | 0.8028 | 0.6735 | 0.7956 | 0.3122 | 0.4967 | 0.3588 | 0.3465 | 0.6877 | 0.7997 | 0.3897 | 0.4747 | 0.4938 | 0.4503 | 0.4514 | 0.4762 | 0.538 | 0.4818 | 0.3191 | 0.316 | 0.3116 | 0.2842 | 0.2825 | 0.2301
Cuitlahuac 869 SV | 1.3335 | 1.1249 | 0.7496 | 0.449 | 0.33098 | 0.22898 | 0.15844 | 0.10965 | 0.075891 | 0.052534 | 0.03637 | 0.025183 | 0.017439 | 0.012078 | 0.008367 | 0.005796 | 0.004016 | 0.002783 | 0.001929 | 0.001337 | 0.000927 | 0.000643 | 0.000446 | 0.000309 | 0.000214 | 0.000149 | 0.000103 | 7.2e-05
Cuitlahuac 869 Antes Venturi | 1.3335 | 1.1249 | 0.7496 | 0.449 | 0.33098